## Slide 1: Équipement de protection individuelle (EPI) au PoE : Mettre et retirer l’EPI
[Date]
Notes: We have learned about the specific types of PPE you need at a POE, and also how to check readiness levels for stocking it. Now we will discuss the most important part—how to safely don, or put on, and doff, or take off, PPE.

## Slide 2: Objectifs d’apprentissage
Apprenez comment mettre et retirer l’EPI en toute sécurité
  Déterminer l’ordre exact des étapes à suivre pour mettre et retirer l’EPI
  Présenter le « système de binôme » et son utilité pour mettre et retirer l’EPI
Notes: Our learning objectives are short for this module, and they come down to this---how can I don and doff PPE correctly and safely?
We’ll discuss why this is so important, as well as the correct order of steps to follow.
We’ll even demonstrate that with you, and walk you through those steps.
We’ll talk about the “buddy system” of donning and doffing PPE, and we’ll practice that as well.
We’ll give you the opportunity to don and doff PPE. We’ll perform it for you one more time, and then we’ll evaluate you donning and doffing through use of the checklist.

## Slide 3: Pourquoi est-ce si important de mettre et retirer l’EPI en toute sécurité ?
L’EPI vous protège de la maladie et protège les autres personnes avec lesquelles vous pouvez être en contact
Une petite coupure dans l’EPI peut entraîner une infection
Il existe de nombreux exemples de propagation de la maladie lorsque l’EPI n’est pas porté correctement
Notes: Let’s review why this is so important.
PPE gives you the best protection possible from disease. As part of your job, you are exposed to ill people regularly. Through the proper use of PPE, you can decrease the chance that you get ill.
And by reducing the chance you get ill, you are also reducing the likelihood that people around you get ill.
But just wearing PPE isn’t all. You have to don and doff it in the right order, and ensure the PPE is clean and not torn. If there is one small breach in the PPE, it is not effective. There are multiple examples of disease spread documented when PPE is not worn properly.
Remember when donning and doffing PPE to be careful of cross-contamination, it is often just as important how you doff your PPE as it is how you don it. Cross-contamination can lead to disease spread just as easily as not correctly wearing PPE.

## Slide 4: Étapes pour mettre l’EPI
Notes: Now we will go over the steps for donning PPE in detail. Please turn to your job aid on donning and doffing PPE in your handbooks.
Call up 2 additional facilitators to come to the front of the room. You are also going to see us taking a few short videos of our instructors performing these tasks. We can try to share these with you after the training. Ask videographer to come to front of room and take small, 30 second to one minute clips of each step.
(Facilitators’ names) will be demonstrating the action steps of putting on the PPE, and we will walk you through each step.

## Slide 5: Étape 1 : Lavez-vous les mains !
Pour tous - évaluations principales, évaluations secondaires et chaque fois que les mains peuvent être sales !
Une bonne hygiène des mains est la première et la dernière ligne de défense contre la propagation de la maladie
Lavez-vous les mains avec de l’eau et du savon pendant au moins 20 secondes
  Si vous n’avez pas d’eau et de savon, utilisez un gel à base d’alcool pour les mains (avec au moins 60 % d’alcool)
Si les mains sont visiblement sales, lavez-les avec du savon
et de l’eau chaude
Enlever les bijoux ou éléments susceptibles de gêner
avec des gants plus tard
OU
Notes: Step 1 isn’t putting anything on—it’s washing your hands! You’ll see this step again at the very end when we are taking off PPE.
It is preferred that you wash your hands with soap and water, although if you do not have access, hand sanitizer will work.
Make sure your hands are completely dry before moving forward.
We also advise that you remove any jewelry, such as rings, before putting on gloves, as the ring may cause the glove to tear.
We are not going to demonstrate this task in detail, but please remember to do it every time.

## Slide 6: Étape 2 : Combinaison
Généralement pour les évaluations secondaires/contrôle (sauf si vous savez à l’avance que les liquides organiques sont problématiques)
Enfiler les bras par les emmanchures (l’ouverture de la combinaison est dans le dos)
Nouer par derrière au niveau du col et à la taille
Si la combinaison est trop petite, utiliser deux blouses, la première attachée devant et la deuxième attachée dans le dos
Notes: Now we get into the actual donning.
As we mentioned earlier, a gown is mostly used during more thorough assessment, such as secondary assessments. It is not always during primary assessments, although if you know in advance that someone is bleeding or vomiting, please consider using it even during a primary assessment. Remember this when you are being tested later today, and we give you a scenario. There are some situations where you need a gown, and others when you do not.
Now the facilitators will demonstrate putting on a gown. I am going to verbally instruct them on each step.
They first need pick up a gown and inspect it for any holes or tears. Facilitator picks up gown and inspects.
Next, if the gown is free of tears, they put one arm in at a time in the arm holes, noting that the gown is to be fastened in the back. Facilitator takes gown and inserts arms, attempting to fasten in the back.
But what if the person can’t reach in the back to tie the gown? This is where a “buddy” can be of help, which we will talk about soon. Ask facilitator to ask second facilitator to help tie the ties. Now, it is important that your “buddy” also has performed step 1, which was what? Allow class to answer. Yes, washing hands.

## Slide 7: Étape 3 : Masque respiratoire N95 (Remarque importante : assurez-vous de faire un essai d’ajustement avant de porter un masque respiratoire)
Le faire chaque fois que vous portez un masque respiratoire N95
Vérification de l’étanchéité
  Étape 1 : Est-il propre ?
  Étape 2 : Est-il correctement placé ?
  Étape 3 : Est-il adapté ?
Ajustement correct
  Serré
  On ne doit pas détecter les odeurs extérieures
  Fuite minimale à l’inhalation
  Différentes tailles disponibles
  Situations où le N95 ne convient pas
Notes: Okay, step 3. Now, as we discussed earlier, respirator usage definitely depends on the situation. They are usually used in a secondary assessments or screenings, particularly if there is an infectious disease threat, but there might be a possibility you use it during a primary assessment as well if you suspect that it is needed at the time.
We are going to have one of our facilitators demonstrate how to put on a respirator.
But before we do so, who can tell me the differences between a respirator and a facemask? We went over this earlier today. Allow for responses.
The difference is that a respirator is the best way to protect YOU from inhaling small particles of germs, but a surgical mask is the best way to protect an ill person from expelling or sharing those germs with others.
.(Ask second facilitator to demonstrate steps for wearing a N95 and a seal check as you go over them.) Ask participants to review user seal check job aid.
Is it clean?: First inspect the respirator. Is it clean? Are there any visible tears, damage, or wear? If yes, dispose of the respirator. If the respirator comes flat, open up the folds completely.
Is it on correctly?: Using one hand, place the respirator on your face.
  The nosepiece should be held by your fingertips and the headbands should hang freely. Do not touch the inside of the respirator if you can avoid it.
  The nosepiece should cover the bridge of your nose and the bottom of the respirator should cup your chin.
  Pull top strap over your head, it should rest above your ears.
  Pull bottom strap over your head, around your neck, and below your ears.
  Do not cross straps.
  Make sure your mouth and nose are fully covered by the respirator- there should be no gaps under the chin or around the nosepiece
  Mold the nose strip to your nose- start at the bridge of your nose and slide your fingertips down the top of the mask to ensure a tight fit
Does it fit?: Cover surface of respirator with hands.
  Positive pressure- gently exhale. Does the N95 expand slightly?
  Negative pressure- take a quick, deep breath. Does the N95 dip in slightly?
  Are there any air leaks around eyes? Around chin?
  Can you smell outside smells?
  If yes to last two questions- readjust and try again. If there is still leakage you will need to try a different size N95 if available.
Can you think of a situation where a N95 will not work? (Wait for responses- Possible responses could include- when the size is incorrect, when someone has facial hair or jewelry that prevents the respirator from sealing correctly, etc.)

## Slide 8: Étape 3 : Masque respiratoire N95 (suite)
Trois facteurs clés requis pour que le masque respiratoire soit efficace
① Le masque respiratoire doit être correctement placé et porté pendant l’exposition.
③ Le filtre respiratoire doit capturer plus de 95 % des particules de l’air qui y passe.
② Le masque respiratoire doit être ajusté contre le visage de l’utilisateur, pour s’assurer qu’il n’y a pas d’interstice entre la peau de l’utilisateur et le masque.
*Si votre masque a une barre métallique ou un coussin de nez moulé, il doit reposer sur le nez et non sur le menton.
Correct*
Mauvais

## Slide 9: Étape 4 : Écran facial ou lunettes
Uniquement pour les évaluations secondaires/le contrôle
Si un écran facial est utilisé, positionner celui-ci sur le visage et le fixer au front à l’aide du bandeau
Si des lunettes de protection sont utilisées, positionner celles-ci sur les yeux et les fixer sur la tête derrière les oreilles ou à l’aide du bandeau
Ajuster confortablement l’écran facial
Notes: Next is our face shield, or our goggles. As you might remember from earlier this morning, goggles or face shields are not necessary during initial assessments as you most likely will not have access to them. You might use them in secondary assessments if the spillover of bodily fluids is a concern.
Let’s first use the face shield. The face shield should have a headband with it. First position the shield over your face and secure the headband on your brow. (Facilitator secures face mask).
Next, let’s use the goggles. Find the band of the goggles and pull them over your head, ensuring a tight fit. You may have to adjust the straps to fit your head. (Facilitator pulls band of goggles over their head but the band is purposefully big. They use sliders on the strap to make the band smaller to fit).

## Slide 10: Étape 5 : Gants
Pour les évaluations principales ET secondaires/le contrôle
Connaissez votre taille de gant !
Enfiler les mains dans les gants
Étendre pour couvrir le poignet de la blouse (si vous portez une blouse)
Notes: Last but not least is gloves! They are used in every ill person encounter, whether it is the first time you are seeing them—initial or primary—or in a more thorough assessment.
Putting on gloves is easier than taking them off---remember this! It is also good to remember your glove size. We all have different hand sizes, so we’ll make sure each of you know your glove size before you leave. You should ideally have access to that size of glove.
I’ll now ask both our facilitators to put on gloves. Look at them insert their hands into the gloves (facilitators do so) and then extend the glove to make sure to cover the wrist area of their gown (facilitators do so). This it to ensure you have no areas of your skin uncovered.
If you are not wearing a gown, think about just extending the glove to your wrist, or the area you would normally wear a watch.
And as removing gloves is very difficult, we’re going to give you a little extra practice now. Hand out gloves to all. Go ahead and put them on, and keep them on until for a few minutes.
That completes our demonstrators putting on, or donning, PPE. But now….

## Slide 11: Étapes pour retirer l’EPI
Notes: They must remove it, or doff it!
Donning mistakes may cause you to be exposed, but even if you don 100% perfectly, if you doff incorrectly, you exposed yourself. This is because you may have been exposed to germs or bodily fluids during an ill passenger risk assessment, and by removing your PPE incorrectly, you may accidentally spill some of that on your bare skin. Follow these steps exactly to make sure that does not happen.

## Slide 12: Étape 1 : Retirer les gants
L’extérieur de vos gants est contaminé !
En cas de contamination des mains durant le retrait des gants, lavez-vous immédiatement les mains ou utilisez une solution hydro-alcoolique pour les mains
En utilisant une main gantée, saisissez la paume de l’autre main gantée et retirez le premier gant
Tenez le gant qui a été retiré dans la main toujours gantée
Faites glisser les doigts de la main non gantée sous ce qu’il reste de l’autre gant au niveau du poignet et faites passer le deuxième gant sur le premier gant
Jetez les gants dans une poubelle
Notes: Notice that these steps are in the exact opposite order of donning steps. That’s a good way to remember the order of events!
When you remove PPE, you need to remember that the outside of your gloves are contaminated—they are covered with germs. Let’s think about the worst case scenario—they are covered with bodily fluids like blood, vomit, or feces. In that case, it is very easy and horrifying to see exactly when you make a mistake and you get germs on you.
So that’s what we’re going to do. We’re going to make it a little harder for our facilitators/demonstrators now because we are going to mimic their gowns and their gloves being contaminated…..with ketchup. Pour ketchup on gloves and gown.
The outside of their gloves are definitely contaminated now. You may not have ketchup on your gloves, but think as though you do. Follow these steps along with our demonstrators.
Let’s see how they remove them.
The first step is to used one of your gloved hands to grasp the palm area of your other gloved hand. Ask facilitators to do this, making sure they grasp the palm area of their hand.
Next, peel the first glove off—carefully. Ask facilitator to peel off glove.
One glove is now off. But don’t throw it away! Hold that removed glove in your hand that still has the glove on. Facilitator holds glove in gloved hand.
This is the hardest step. Use your fingers of your hand with no glove to carefully slide a finger inside the wrist of your remaining glove. Peel that glove off while pulling this glove over your other glove in your hand. Both gloves should now end up inside out after they have been removed. Ask facilitator to do this and repeat those steps aloud to the participants.
Now you should have two clean hands.

## Slide 13: Étape 2 : Enlever les lunettes de protection ou l’écran facial
L’extérieur des lunettes de protection ou de l’écran facial est contaminé !
En cas de contamination des mains durant le retrait des lunettes de protection ou de l’écran facial, lavez-vous immédiatement les mains ou utilisez une solution hydro-alcoolique pour les mains
Retirez les lunettes de protection ou l’écran facial en le saisissant à l’arrière et en soulevant le bandeau ou les branches
Si l’équipement est réutilisable, placez-le dans le conteneur prévu à cet effet pour retraitement Autrement, jetez-le dans une poubelle
Notes: Next is taking your goggles or face shield off. Remember that the outside surfaces of these are likely contaminated. If for some reason during this process your hands ever get contaminated, stop what you are doing and wash them.
Here, start by lifting the back strap of your shield or goggles, which is on the back of your head. Ask facilitator to perform this step.
These PPE can technically be reused, but if there are a lot of contaminants on them or they are badly damaged, throw them away in a biohazard container. Even if they appear clean, they still are likely contaminated, and will need cleaning.

## Slide 14: Étape 3 : Retirez la blouse
Le devant et les manches de la blouse sont contaminés !
En cas de contamination des mains durant le retrait de la blouse, lavez-vous immédiatement les mains ou utilisez une solution hydro-alcoolique pour les mains
Détachez les attaches de la blouse en vous assurant que les manches ne touchent pas votre corps lorsque vous attrapez les attaches
Enlevez la blouse par le col et les épaules, en ne touchant que l’intérieur de la blouse
Retournez la blouse à l’envers
Pliez-la ou roulez-la en boule et jetez-la dans une poubelle
Notes: Now we are removing our gown that was contaminated with all the ketchup. Again, just as before, if your hands get contaminated in this step, wash them immediately.
Start in reaching in the back and untie the types, but make sure to reach your arms high so you don’t have your contaminated sleeves hit your body. Ask facilitator to do this, verbally sharing how they are lifting their arms to avoid this contamination.
Now you have access to the inside of the gown. Use your grip on the inside of the gown to pull the gown away from your neck and shoulders, turning it inside out. Ask facilitator to perform this step as stated, verbally sharing how they are using the inside of the gown to pull it off.
You are not done yet! Make sure to fold the gown into a bundle—making sure the inside of the gown is outside—and discard it in a waste container. Ask facilitator to perform this step as stated.

## Slide 15: Étape 4 : Retirez le masque facial ou respiratoire
Le devant du masque/respirateur est contaminé – NE PAS TOUCHER !
En cas de contamination des mains durant le retrait du masque/respirateur, lavez-vous immédiatement les mains ou utilisez une solution hydro-alcoolique pour les mains.
Saisissez les attaches ou élastiques du bas du masque/respirateur, puis celles du haut, et retirez-le sans toucher le devant.
Jetez-les dans une poubelle
Notes: Now we remove our face masks, which are our respirators or surgical masks. Do not touch the front of the mask or the respirator—remember this, as it is contaminated!
Surgical masks should have two ties. First grasp the ones at the bottom, and then the top, to remove the mask which paying special attention not to touch the front. Ask facilitator to perform this task, talking their way through the step, to ensure the front of the mask is not touched.
If you have an respirator, most likely an N95, remove by pulling the bottom strap first over the back of the head, followed by the top strap. Don’t let go of the top strap as you are now using it to hold the respirator. Ask the facilitator to perform this task, talking aloud through taking the bottom strap off first, then the top strap.
Finally, discard the mask in a waste container. Remember to only touch the straps when doing this.

## Slide 16: Étape 5 : Lavez-vous les mains !
Pour tous : évaluations primaires, évaluations secondaires et chaque jour !
Une bonne hygiène des mains est la première et la dernière ligne de défense contre la propagation de la maladie
Lavez-vous les mains avec de l’eau et du savon pendant au moins 20 secondes
  Si vous n’avez pas d’eau et de savon, utilisez un gel à base d’alcool pour les mains (avec au moins 60 % d’alcool)
Si les mains sont visiblement sales, lavez-les avec du savon et de l’eau chaude
OU
Notes: And the last step here is the first step in donning….wash your hands! This is a repeat of the first slide but it is very important to remember!!

## Slide 17: Le « système de binôme » pour mettre et retirer l’EPI
Notes: Before we break out into groups for practice and evaluation of you donning and doffing, let’s discuss the buddy system.

## Slide 18: Qu’est-ce que le système de binôme ?
Une méthode dans laquelle une personne en aide une autre pour mettre un EPI
Un binôme peut également aider pour :
  Inspecter l’EPI pour les coupures, déchirures ou trous
  Attacher les combinaisons, etc.
  S’assurer que les masques sont bien ajustés
    Demandez à votre binôme : « As-tu vérifié l’étanchéité ? »
Notes: The buddy system is a way to help your colleagues with donning and doffing PPE. One person can assist another, particularly if the person you are assisting has primary responsibility for caring for an ill person.
In addition to helping don the PPE, a “buddy” can inspect that PPE to ensure there are no tears or holes in the PPE to ensure maximum coverage.

## Slide 19: Répartition des groupes et évaluations de l’EPI

## Slide 20: S’entraîner à mettre et retirer un EPI !
Rassemblez vos groupes* à côté de chaque pile d’EPI disponibles
Chaque groupe aura [nombre-nombre*] d’animateurs
Votre animateur démontrera à nouveau le processus complet pour mettre et retirer l’EPI
*Nombre suggéré de participants par groupe : 5
Nombre suggéré d’animateurs par groupe : 1 à 2
Notes: See facilitator’s guide for detailed notes on this activity.