## Slide 1: Contrôle de la température et considération sur les thermomètres
FORMATION POUR LE SECTEUR DE LA SANTÉ
Date
Notes: This section describes an important part of conducting a risk assessment of an ill traveler – taking temperatures.

## Slide 2: Objectifs d’apprentissage
Décrire les principales méthodes de prise de température à un PoE
Définir le seuil de température pour l’orientation et discuter s’il diffère selon la maladie
Expliquer le rôle de la température dans la surveillance
Notes: Our first objective for is to describe the primary methods of temperature taking at a POE.
We’ll then get into defining the temperature cutoff for referral and discuss if it differs according to the illness.
Finally, we’ll explain the role of temperature taking in surveillance and break into groups to practice proper temperature taking methods.

## Slide 3: Fièvre
La température corporelle moyenne est de 37 ºc
La fièvre est une température corporelle mesurée au-dessus de la normale
  La fièvre est le symptôme le plus fréquent d’une maladie infectieuse
  Parmi les autres causes de fièvre, on trouve d’autres pathologies, un traumatisme ou une blessure grave ou certains médicaments
Notes: So what is fever? It’s just a measured body temperature above the normal, which is 37 degrees Celsius.
Fever is the most common sign of infectious disease. In fact, can anyone raise their hand and share an infectious disease that has fever as a sign? Allow class to raise hands. Expected responses: measles, meningitis, Ebola/viral hemorrhagic fevers, etc. We will discuss clinical diagnostic criteria tomorrow, but remember that for the vast majority of infectious diseases, fever is a sign.
With that said, there are other conditions outside of infectious diseases that could still cause fever. Other medical conditions, severe trauma that your body is fighting—hence the fever—or even some medications can cause your fever to rise.

## Slide 4: Rôle du contrôle de la température dans la surveillance de la santé
Il est régulièrement utilisé au PoE pendant l’évaluation des risques d’un voyageur malade
Prenez toujours la température pendant une évaluation des risques
Elle peut être utilisée au cours d’un contrôle spécifique à une maladie au PoE
Notes: Temperature assessment is common at POE and it is part of your role as [POE health agency] to do so during ill person risk assessments. Every time you get referred an ill passenger, you take a temperature. No questions asked. It is easy to do with the materials available to you.
Every now and then, the country may ask the POE to conduct temperature screening, which is usually the result of a local outbreak or, less frequently, WHO telling us to via a Public Health Emergency of International Concern declaration. When that occurs, you are charged to take temperatures of a greater amount of people. Usually, in these situations, there is specific guidance for this procedure.

## Slide 5: Le contrôle de la température ne constitue qu’une partie de l’évaluation des risques
Même le meilleur contrôle de température « manquera » certains cas de maladies infectieuses
  Les voyageurs peuvent prendre des médicaments pour masquer leur fièvre
  Les voyageurs peuvent avoir été infectés par la maladie, mais ne pas présenter encore de symptômes (c.-à-d., ils sont en phase d’incubation)
  Certaines infections peuvent ne pas présenter de symptômes (c.-à-d. être asymptomatiques), comme le COVID-19.
  Certaines infections ne s’accompagnent pas toujours de fièvre, même lorsqu’elles sont symptomatiques (par ex., grippe)
Le contrôle de la température doit être une étape nécessaire, mais pas la seule, d’une évaluation des risques pour la santé
  Relever également les antécédents médicaux, l’historique des déplacements, l’historique des symptômes et les antécédents d’exposition
Notes: Before we get into the specifics of taking a temperature, I want to stress that it is a necessary part, but not the entirety of the ill passenger risk assessment process. Some people may be infected with a disease, but are not showing a fever. Why? Well, some could try to mask it by using paracetamol or other medications. Others may have already been exposed to disease and are infected with the disease, but may not be showing symptoms yet. This is known as “incubating” disease.
Different diseases behave differently in respect to fever and symptoms. One disease that is well known for being infectious while someone is incubating, or not yet showing symptoms, is influenza. However, Ebola can only be spread when someone is symptomatic. Also, some diseases may be spread while an individual is asymptomatic (showing no symptoms), such as with COVID-19.
Understanding these limitations, it is important to collect other information from people during risk assessments, like their past medical history, travel history, and exposure history. Temperature is only one part of the complete puzzle.

## Slide 6: Présentation des thermomètres sans contact
Un moyen de prendre la température d’une personne sans la toucher
Identique en précision aux thermomètres à contact
Il est très important de connaître le modèle spécifique du thermomètre sans contact
  Techniques d’étalonnage
  Où mesurer la température
Notes: Now, all of you should have access to a non-contact thermometer at your POE. Is that correct? Allow for responses.
Thus, you should be aware of their benefits! They are a great way to take someone’s temperature without touching them, so this is very helpful for infection control purposes. They are similar in accuracy to contact-based thermometers without the cleanup and infection risk involved.
The main aspect you need to know about these thermometers is their model. There are many different types of non-contact thermometers, and each has slightly different ways of taking the temperature. For instance, some require that you take the temperature at the side of your head, and others require that you take it at the front of your head—look at the photos here for an example. Different models also differ in their calibration techniques, or the way you get the thermometer ready to take a temperature.

## Slide 7: « Seuils » de température
Lorsque vous n’êtes pas sûr(e) de la maladie en question, habituellement une température d’environ 37,5 ºc, 38 ºc ou plus est une indication que la personne est malade.
Une personne peut toujours être infectieuse avec une température inférieure. C’est pourquoi il est si important de recueillir les autres informations
Les « seuils » de température sont plus utiles lors des événements de dépistage en masse, comme dans le cas du dépistage d’Ébola en RDC
Si une température est inférieure à 35 ºc, reprenez la température
Notes: We also wanted to give a quick note on temperature cutoffs. This is more useful during mass screening events like the Ebola outbreak than during routine times, but, if a person has a temperature beyond 37.5°C or 38°C, they can be sick and infectious. Even if they have a temperature below that level, they can still be sick and infectious, and this is again is reason to collect additional information like travel history, medical history, and exposure history.
However, if someone has a measured temperature below 35°C, measure it again. Most of us in this room would be dead if our temperatures were measured below 35 degrees! This also might be a sign that your thermometers needs to be re-calibrated or needs new batteries.

## Slide 8: Considérations concernant les caméras thermiques/scanners thermiques
Plus fréquents dans les aéroports que dans les autres PoE
Avantages
  Peuvent mesurer la température à partir d’une distance supérieure à celle d’un thermomètre sans contact
  Peuvent « dépister » les personnes plus rapidement que les thermomètres sans contact
Inconvénients
  Coûteux
  Moins précis que le thermomètre sans contact - vérifiez avec un thermomètre sans contact
  Temps considérable pour la configuration et l’étalonnage
  Nécessitent davantage de formation du personnel
Notes: Before we get into practicing measuring temperature, it’s important to quickly discuss thermal cameras, or as you sometimes hear them called, thermal scanners.
These are much more common at airports than at other POE, but they are quickly becoming quite common. Let’s discuss what they can and what they cannot do.
The advantage to these devices are that they can measure temperature from a greater distance than a non-contact thermometer. They also have the ability to screen people much quicker than a non-contact thermometer.
But you need to know their disadvantages. First and foremost, they are not as accurate as a non-contact thermometer. They have not been evaluated to be a primary diagnostic tool for any disease, and while you may be able to get an idea of fever from them, do not rely on them alone. Thus, if someone sets off the thermal camera or scanner with a fever that is above a pre-set threshold, most likely 37.5°C or 38°C, verify that temperature with a non-contact thermometer, which is more accurate.
Beyond this disadvantage, thermal cameras also must be highly calibrated and regularly maintained

## Slide 9: Démonstration du thermomètre sans contact
Par deux animateurs
Lire les directives d’étalonnage de thermomètre et de prise de température à haute voix
Notes: Let’s now re-familiarize ourselves with taking a temperature properly. Ask 2 additional facilitators to come to the front of the room to assist. Also ask videographer to come back to the front of the room to take short videos.
We are going to demonstrate the process of taking a temperature. First, our facilitator/demonstrator is looking at the thermometer to ensure it has batteries and is ready for use. Pause to allow demonstrator to view thermometer and review batteries. Now, we need to ensure this thermometer is calibrated according to the instructions.
Allow the demonstrator to read aloud the calibration instructions for this particular thermometer, and have them act out the steps while reading.
Now that the thermometer is calibrated, it is ready for use. Remember to look back at the specific directions for this thermometer to see if you are measuring temperature at the front of the head or the side of the head. Ask the demonstrator to read aloud the instructions on where to take the temperature.
Now, we need to know how far back to stand to take a temperature. Ask the demonstrator to read aloud the instructions on how far back to stand to take the temperature.
Demonstrator takes the temperature and reads aloud to the class the answer. If it is below 35°C, they announce that the thermometer must be calibrated improperly or something must have happened and they take the temperature again. If is between 35-37.5°C, that is fine. If it is above 37.5°C, they want to ask the person additional questions, as they may be sick.

## Slide 10: Activité en groupes : Prises de températures
Retournez dans vos groupes
Un animateur sera assigné à chaque groupe
L’animateur montrera à nouveau la manière précise d’étalonner et de prendre une température ; chaque membre du groupe a la possibilité de s’entraîner
Les membres du groupe seront ensuite évalués sur les méthodes précises de prise de température
Notes: Now for our activity! We’ll break into our groups again and each group will have a facilitator assigned to them.
Within the group, your facilitator will again demonstrate the process of taking a temperature. You then can have a chance to practice, without being graded, in taking temperatures. After practicing, each group member then will be evaluated on:
-Accurately turning on the thermometer and waiting until it was properly calibrated to take temperature. This includes checking the batteries.
-Taking temperature in the accurate location on the head
-Standing back in the appropriate location and not right next to the person (e.g. extending arm) for infection control purposes
-Reading out the temperature and then accurately interpreting the temperature (e.g. if below 35°C retaking, if 35-37.5°C okay, if past 37.5°C referred or asked for additional health surveillance measures)
Instruct participants to break into groups and follow the facilitators to certain areas of the room. Facilitator then demonstrates the use of the thermometer and allows each participant to practice—without grading—and offers recommendations for refinements and improvements. Each participant gets to practice once.
Then the facilitator needs to use the Temp Taking Evaluation Checklist to evaluate each of the participants.